## Slide 1: FDTD Simulations with Meep

## Slide 2: Meep
FDTD simulation software
Free and open-source
Distributed memory parallelism
Pre-compiled binary packages via conda
Inverse design tools
Python interface

## Slide 3: Check out the website
Documentation
Detailed explanations
Lots of tutorials

## Slide 4: In this video
Show how to setup a scattering simulation in Meep
  scattering geometry
  plane wave source
  scattering & absorption spectrum
  Fourier Transform monitors
  Flux monitors
  Movie monitors
  Materials with dispersion

## Slide 5: Soon…
How to setup a waveguide simulation in Meep
  Waveguide geometry
  Mode source
  Eigenmode expansion monitor
Inverse design with Meep
etc.

## Slide 6: Scattering Problem
Plane wave incident on scatterer
Want to know:
  How much light is scattered
  How much light is absorbed
Erik Abenius, Time-Domain Inverse Electromagnetic Scattering using FDTD and Gradient-based Minimization (2004)

## Slide 7: Scattering FDTD simulation
nanoparticle

## Slide 8: Scattering FDTD simulation
nanoparticle
Total-field scattered-field source

## Slide 9: Scattering FDTD simulation
nanoparticle
Total-field scattered-field source

## Slide 10: Scattering FDTD simulation
nanoparticle
Total-field scattered-field source
Scattering monitor

## Slide 11: Scattering FDTD simulation
nanoparticle
Total-field scattered-field source
Scattering monitor
Absorbing Boundary Conditions
Absorbing Boundary Conditions
Absorbing Boundary Conditions
Absorbing Boundary Conditions

## Slide 12: Scattering FDTD simulation
nanoparticle
Total-field scattered-field source
Scattering monitor
Absorbing Boundary Conditions
Absorbing Boundary Conditions
Absorbing Boundary Conditions
Absorbing Boundary Conditions
Absorption monitor

## Slide 13: Scattering Meep FDTD simulation
Scattering geometry (nanoparticle)
Total-Field Scattered-Field (TFSF) source
Scattered box monitor (scattered field)
Absorption box monitor (total field)
Perfectly matched layer (PML) absorbing boundary conditions

## Slide 14: Scattering Meep FDTD simulation
nanoparticle
Total-field box monitor
PMLs
Plane-wave source
PMLs

## Slide 15: Scattering Meep FDTD simulation
nanoparticle
Total-field box monitor
PMLs
Plane-wave source
PMLs
How do we isolate scattered light?

## Slide 16: Scattering Meep FDTD simulation

## Slide 17: Scattering Meep FDTD simulation
We know this
We can find this

## Slide 18: Scattering Meep FDTD simulation
Run 2 simulations!
Empty simulation -
Normal simulation -

## Slide 19: Scattering Meep FDTD simulation
- We will be using flux monitors for scattering/absorption
flux monitors

## Slide 20: Scattering Meep FDTD simulation
We will be using flux monitors for scattering/absorption
Monitors calculate the electromagnetic power that travels through the monitor plane

## Slide 21: Scattering Meep FDTD simulation
We will be using flux monitors for scattering/absorption
Monitors calculate the electromagnetic power that travels through the monitor plane
Power travelling through y-z Flux monitor
(in the x-direction)
Integral of x-component of Poynting vector integrated over the montor surface
Flux monitor

## Slide 22: Scattering Meep FDTD simulation
We will be using flux monitors for scattering/absorption
Monitors calculate the electromagnetic power that travels through the monitor plane
Power travelling through y-z Flux monitor
(in the minus x-direction)
Integral of x-component of Poynting vector integrated over the montor surface
Flux monitor

## Slide 23: Scattering Meep FDTD simulation
We will be using flux monitors for scattering/absorption
Monitors calculate the electromagnetic power that travels through the monitor plane

## Slide 24: Scattering Meep FDTD simulation
We will be using flux monitors for scattering/absorption
Monitors calculate the electromagnetic power that travels through the monitor plane
Meep has functions for this
  When preparing the second simulation (with scatterer), provide the flux monitor with the fields from the first (empty-domain) simulation
data from empty simulation
monitor for scattering simulation

## Slide 25: Scattering Meep FDTD simulation
We will be using flux monitors for scattering/absorption
Monitors calculate the electromagnetic power that travels through the monitor plane
Meep has functions for this
Meep does this calculation in the backend
And returns only the scattered power

## Slide 26: Scattering Summary
Run 2 simulations: 1) just to calculate and 2) for

## Slide 27: Scattering Summary
Run 2 simulations: 1) just to calculate and 2)
Use Meep tools to get scattered power for each Flux monitor

## Slide 28: Summary
Run 2 simulations: 1) just to calculate and 2)
Use Meep tools to get scattered power for each Flux monitor
Calculate the scattered Power

## Slide 29: Summary
Run 2 simulations: 1) just to calculate and 2)
Use Meep tools to calculate for each Flux monitor
Calculate the scattered Power
Normalize by source intensity to get scattering cross section

## Slide 30: Absorption
Same thing, but using only the total-field fluxes

## Slide 31: Practical notes
Meep uses special units
  Speed of light

## Slide 32: Practical notes
Meep uses special units
  Speed of light
Length-distances are in microns
Frequencies are
  Wavelength in microns

## Slide 33: Practical notes
Meep uses special units
  Speed of light
Length-distances are in microns
Frequencies are
  Wavelength in microns

## Slide 35: Practical notes
Meep uses special units
The simulation domain is centered at 0
  If the simulation domain is

## Slide 36
Size_x
Plane wave source
Size_y
PML
PML

## Slide 37: Code break!